## Slide 1: Gates
Let’s examine the processing of the following six types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR
Typically, logic diagrams are black and white, and the gates are distinguished only by their shape

## Slide 2
NOT Gate -- Inverter
X
Y
0
1
1
0

## Slide 3: NOT Gate
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

## Slide 4: AND Gate
AND
X
Y
Z
Z = X & Y
X Y Z
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 5: AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0
Figure 4.2 Various representations of an AND gate

## Slide 6: OR Gate
OR
X
Y
Z
Z = X | Y
X Y Z
0 0 0
0 1 1
1 0 1
1 1 1

## Slide 7: OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1
Figure 4.3 Various representations of a OR gate

## Slide 8: NAND Gate
NAND
X
Y
Z
X Y Z
0 0 1
0 1 1
1 0 1
1 1 0
Z = ~(X & Y)
nand(Z,X,Y)

## Slide 9: NOR Gate
NOR
X
Y
Z
X Y Z
0 0 1
0 1 0
1 0 0
1 1 0
Z = ~(X | Y)
nor(Z,X,Y)

## Slide 10: NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively
Figure 4.5 Various representations of a NAND gate
Figure 4.6 Various representations of a NOR gate

## Slide 11: Exclusive-OR Gate
X Y Z
XOR
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0
Z = X ^ Y
xor(Z,X,Y)

## Slide 12: XOR Gate
XOR, or exclusive OR, gate
  An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise
  Note the difference between the XOR gate and the OR gate; they differ only in one input situation
  When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0

## Slide 13: XOR Gate
Figure 4.4 Various representations of an XOR gate

## Slide 14: Exclusive-NOR Gate
X Y Z
XNOR
X
Y
Z
0 0 1
0 1 0
1 0 0
1 1 1
Z = ~(X ^ Y)
Z = X ~^ Y
xnor(Z,X,Y)